## Slide 1
L’innovazione nell’efficienza energetica
Infrastructures Business Unit

## Slide 2
PREMESSA
Decreto 24 dicembre 2015 – Criteri Ambientali Minimi “affidamento dei servizi di progettazione, dell'esecuzione di lavori pubblici e la gestione dei relativi cantieri”
Decreto 23 dicembre 2013 – Criteri Ambientali Minimi: “illuminazione pubblica e affidamento dei servizi di progettazione di impianti di illuminazione pubblica”
Decreto Ministeriale del 26 giugno 2015 “Applicazione delle metodologie di calcolo delle prestazioni energetiche e definizione delle prescrizioni e dei requisiti min. degli edifici”.
Panorama normativo e ruolo della ricerca

## Slide 3
Envision
Auto-Dan
Rinno
Contents

## Slide 4
ENVISION PROJECT
Energy harVesting by Invisible Solar IntegratiON in building skins
For reaching 2050 EU energy-neutrality goals, solar energy harvesting from all building surfaces should be maximized
ENVISION technologies exploit the near-infrared (NIR) solar radiation, constituting roughly the 50% of the solar energy spectrum.
Active harvesting of the solar radiation from all the building surfaces, while retaining aesthetic aspects.

## Slide 5
ENVISION PROJECT
PV harvesting glass
Façade solar collectors with NIR absorbing colored coatings
Smart ventilated window

## Slide 6
Outside
Inside
ENVISION PROJECT
Smart ventilated window
Designed and manufactured by BGTec
Triple glazed window that harvests the solar radiation for space heating and DHW purposes
Aims to TRL7 (system prototype demo in operational environment)
Currently tested in Savona University Campus
Enables using also glazed surface for energy production

## Slide 7
ENVISION PROJECT
Smart ventilated window
TES
Winter Mode:
Warm air to indoor ambient
No hot water
Summer Mode:
No indoor ambient conditioning
Hot water production
Pump ON only in Summer Mode
Winter mode:
The window works to mantain the required setpoint temperature in the room
Summer mode:
The window provides hot water through a air-water HX.
Notes: Thanks to this module it is possible to use actively also the glazed parts of an envelope. In case of renovation the building energy consumptions can decrease significantly for a dual perspective:
Reduction of building energy demand (triple glazed unit)
Production of thermal energy from renewable source
Applicazioni: uffici con grosse superfici vetrate.
Considering office buildings, the yearly thermal demand can be supplied only by Smart Ventilated Window if R is around 0,9
Where:
𝑅= (𝑆𝑜𝑢𝑡ℎ𝑂𝑟𝑖𝑒𝑛𝑡𝑒𝑑 𝐺𝑙𝑎𝑧𝑒𝑑 𝐹𝑎ç𝑎𝑑𝑒 [𝑚^2])/(𝐵𝑢𝑖𝑙𝑑𝑖𝑛𝑔 𝑎𝑟𝑒𝑎 [𝑚^2])

## Slide 8
ENVISION PROJECT
Sensors for indoor comfort evaluation
Control system
Blowing grid
Suction grid
Water circuit for summer mode

## Slide 9
ENVISION PROJECT
PV harvesting glass
Pilkington Offices
(Netherland + Austria)
System incorporated at SolarBEAT and AUSTRIA Demo
Shading effects investigated
Incorporation within frames has been investigated

## Slide 10
ENVISION PROJECT
Façade solar collectors with NIR absorbing colored coatings
Netherlands residential Demo (North EU Demo)
Italian educational building (Southern EU Demo)
Testing in real environment (TRL8)
Link to district network and grid (Italy, University of Genoa Savona Campus)
Real case study of a renovation action Row Dwellings, Helmond- & Eindhoven

## Slide 11
AUTO – DAN PROJECT
Objectives:
Create a flexible smart hardware infrastructure that can be applied to all small-to-medium sized buildings
Develop an interoperable software architecture that can provide all the analytical capabilities needed to self-assess and self-optimise buildings in the EU
Deliver Augmented Intelligence(AuI) solutions to enable buildings and their users to become self-optimizing
Create a live self-energy assessment method that incorporates operational monitoring, appliance/system performance and smart capabilities that will improve the accuracy of current energy assessment procedures

## Slide 12
AUTO – DAN PROJECT
The self-energy assessment methodology

## Slide 13
AUTO – DAN PROJECT
Demand response program and SRI calculation

## Slide 14
AUTO – DAN PROJECT
Building-level performance indicators - the dashboard could show the difference between the results of the calculated energy consumption for the energy certification and the results derived from the measurements done by the sensors in real-time (Reverse calculation method).
Appliance-level performance indicators: one for each of the analyzed appliances, calculated by comparing the actual performance versus data from the available literature or the models developed in WP3 (also considering Ecodesign indicators)
Smart-readiness evaluations: intersection between the building level and the appliance level -> “gamification scheme” with the indication of the current SRI and the potential one (based on the potential change of some services, together with the indication of potential energy savings)
Financial evaluation (in relation to Demand Response): we could have specific indicators to evaluate the financial impact of energy “choices”, e.g. calculated KPI showing the primary energy saved / potentially saveable by exploiting DR.

## Slide 15
RINNO PROJECT
MicroVent technology
Sector application: MicroVent is used in institutions, school, offices and residential
Benefits to Building owner/residents/tenants/occupants: a cost-effective solution to secure the buildings construction system from unwanted moisture, as well as an added value to the building due to an improved indoor climate building. Minimal space requirements. Improved indoor climate, with lower CO2 level, and better temperature control. Reduced heat and electricity consumption.

## Slide 16
RINNO PROJECT

## Slide 17
RINNO PROJECT
The depth can be adjusted from 500-330mm
And with an external special cover, down to 280mm

## Slide 18
RINNO PROJECT
The most efficient heating solution in Denmark is district heating that does not use gas. The price is down to 0.09 €/kWh
Central ventilation
Decentralized ventilation
with ducts.
Natural ventilation.
Ventilation with MicroVent
Example of building with 12 apartments of 65m2
(With Danish requirement)
The electricity price in Denmark is currently 0.47 €/kWh

## Slide 19
Envision: https://envision-h2020.eu/
Auto-Dan: https://www.autodan-project.eu/
Rinno: https://rinno-h2020.eu/
References

## Slide 20
Michele Mililli
michele.mililli@rina.org